2/26/04

Rev 1.0

CRS

PetaBox Rack Specifications

Scope:

This document defines the specifications of the rack mounted systems which comprise the PetaBox. It is not intended to be a specification for the overall PetaBox system itself.

Storage Capacity:

- Approximately 100TB

- Initial shipments will be with 300G IDE disks, yielding 96TB aggregate capacity

- Later units may be upgraded to larger disk capacity as they become available.

Rack Configuration:

- Standard 19” four-post rack. Rack must be heavy duty to support weight

- The racks must fit into standard 8’ shipping containers. (7’ 6” internal height)

  - 44U rack is ~7’

- Target of 80 nodes per rack

- Weight shall be <2000 lbs

- Rack shall have provisions to support the back of each node without requiring tools or backside access

- Rack shall support the mounting of vertical “0U” power strips

- Thermal Management TBD (rack level fans, panels, etc)

  - Cold air will enter the plenum between nodes

  - Warm air will exit from both sides of the rack

- Each rack shall be self-contained. No racks will require resources from other racks

- Racks shall provide cable management for power and ethernet

Node Configuration:

- Each unit shall be 1U high, half depth

- 1 CPU and 4 hard drives

  - Via ITX form factor

  - Standard Micro ATX form factor also supported

- The Via board shall have the option of a 1G PCI Ethernet NIC

- Standard ATX power supply

- LCD on front panel

- Nodes may be cross-connected via serial ports

- Forced air cooling

  - Cool air enters rear and exits front of each node

- Mounting brackets are located 3” back from front panel (standard)

  - Bracket may also be located flush with front panel

  - Bracket may also be located at approximate center of mass

Power:

- Total power consumption <6KW/rack steady state

  - 20/CPU

  - 20W/4 disks

  - 5W/4 Fans

  - 20W power supply inefficiency

- Disk start-up 25W/Disk

- Entire rack MAY NOT be powered up simultaneously

- Distribution shall be AC, 110V or 220V as determined by location

- Power shall be remotely controllable via switchable power strips

Communications:

- 2 48-Port  or 4 24-Port Switches per rack

- 100M Ethernet from CPUs to local switch

- 1G Uplink from each switch

Performance:

The CPU shall be capable of keeping the 100M Ethernet port fully loaded while transferring files to and from disk

Environment:

- Operating Disk Temp 5-50(C

- Storage Temp –40-70(C

- 0-90% Non-condensing

Operation/Serviceability:

- Operable by single admin

- All components will be readily accessible and easily replaced with simple tools

- Expected disk failure rate of 6%/year

Shipping:

- Each rack shall be individually shippable without requiring the entire PetaBox.

- Rack will be shipped unassembled and then assembled on site.

Cost:

- Target cost < $125K